## Slide 1: Combining Gates & Solving Problems
Computational Thinking, Algorithms & Programming

## Slide 2: Introduction
We have seen how logic circuits can be drawn as diagrams with inputs and outputs, and we can use truth tables to map out the range of possible results from these circuits.
However, we can also combine a series of logic gates to produce more complex circuits.
This allows us to solve problems and identify logical structures in how a computer works.
In this lesson, we’ll learn about:
Combining logic gates to produce simple circuits.
Applying logical diagrams & operators in truth tables to solve problems.

## Slide 3: Producing Simple Circuits
We can start to put logic gates together to make larger circuits.
Each circuit can be represented as a Boolean expression, which will always start with an output, usually called Q.
To solve these, start with the brackets on the inside and work outwards.
Let’s work through three different expressions:
Q = A AND (B AND C)
Q = NOT (A OR B)
Q = (A OR B) AND NOT C

## Slide 4: Worked Example 1
Step 1
Start with the brackets. This is the “B AND C” part.
Figure 1 – An AND gate with the inputs B & C.
Step 2
Add the outer expression; this is the “A AND” part.
Figure 2 – The result of B AND C is used as input on another AND gate with A.

## Slide 5: Worked Example 2
Step 1
Start with the brackets. This is the “A OR B” part.
Figure 3 – An OR gate with the inputs A & B.
Step 2
Add the outer expression. This is the “NOT” part.
Figure 4 – The result of A OR B is then NOTed.

## Slide 6: Worked Example 3
Step 1
Start with the brackets. This is the “A OR B” part.
Figure 5 – An OR gate with the inputs A & B.
Step 2
Add the outer expression. This is the “AND C” part.
Figure 6 – The result of A OR B is used as input on an AND gate with NOT C.

## Slide 7: Solving Problems
We have seen how we can use Boolean algebra to represent some circuits.
We can build up truth tables to show all the inputs and all the possible outputs for any circuit.
We can then use this to work out which combination of inputs will give us a TRUE output.
The way to do this is to start small and build up your truth table column by column.

## Slide 8: Solving Problems
In your exam, you might need to complete a truth table for a given Boolean expression or draw the circuit diagram for a Boolean expression and then plot the truth table.
In order to solve this, you can follow some very simple steps:
Build your inputs
Check to see if any of your inputs have been NOTed
Build your expressions from your initial inputs
Look at the final output
Let’s now work through three example Boolean expressions.

## Slide 9: Worked Example 1
Step 1: Build your inputs
We have two inputs, A and NOT B. So, we need 4 rows.
Step 2: Check to see if any of your inputs have been NOTed
Yes – B has been NOTed, so add a column for NOT B.
Notice how all we have done is flip the B column values.
A | B | Q
1 | 1 | 
1 | 0 | 
0 | 1 | 
0 | 0 | 
A | B | NOT B | Q
1 | 1 | 0 | 
1 | 0 | 1 | 
0 | 1 | 0 | 
0 | 0 | 1 | 

## Slide 10: Worked Example 1
Step 3: Build your expressions from your initial inputs
Now, we need to add the expression by comparing the A column and the NOT B column, which will produce our final output.
As it is an AND gate, the output will be true if both inputs are true.
A | B | NOT B | Q
1 | 1 | 0 | 0
1 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 0

## Slide 11: Worked Example 1
Step 4: Look at the final output
We can see that there is only one possible input to this circuit that gives a TRUE output.
When A = 1 and B = 0.

## Slide 12: Worked Example 2
Step 1: Build your inputs
First, we have three inputs, so let’s see the truth table outline. We should have 8 rows this time.
Step 2: Check to see if any of your inputs have been NOTed
They haven’t so we can skip this step.
A | B | C | Q
1 | 1 | 1 | 
1 | 1 | 0 | 
1 | 0 | 1 | 
1 | 0 | 0 | 
0 | 1 | 1 | 
0 | 1 | 0 | 
0 | 0 | 1 | 
0 | 0 | 0 | 

## Slide 13: Worked Example 2
Step 3: Build your expressions from your initial inputs
First, we have A OR B – ignore C for the moment.
A | B | C | A OR B | Q
1 | 1 | 1 | 1 | 
1 | 1 | 0 | 1 | 
1 | 0 | 1 | 1 | 
1 | 0 | 0 | 1 | 
0 | 1 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 0 | 0 | 

## Slide 14: Worked Example 2
Now, we can add the AND C part, which will produce our final output.
Remember it’s AND – so it’s where we have a 1 in the A OR B column, AND we have a 1 in the C column.
A | B | C | A OR B | Q
1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0

## Slide 15: Worked Example 2
Step 4: Look at the final output
The following table shows the combinations of A, B, and C that give us a TRUE output.
A | B | C
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1

## Slide 16: Worked Example 3
Step 1: Build your inputs
First, we have 3 inputs, so let’s look at the truth table outline. We should have 8 rows.
A | B | C | Q
1 | 1 | 1 | 
1 | 1 | 0 | 
1 | 0 | 1 | 
1 | 0 | 0 | 
0 | 1 | 1 | 
0 | 1 | 0 | 
0 | 0 | 1 | 
0 | 0 | 0 | 

## Slide 17: Worked Example 3
Step 2: Check to see if any of your inputs have been NOTed
Yes – we have NOT B and NOT C, so we add these columns.
A | B | C | NOT B | NOT C | Q
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 0 | 0 | 1 | 
1 | 0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 0 | 
0 | 1 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 
0 | 0 | 0 | 1 | 1 | 

## Slide 18: Worked Example 3
Step 3: Build your expressions from your initial inputs
First, we have A AND NOT B, so we add this column – again, the output is TRUE when both inputs are TRUE, as it is an AND gate.
A | B | C | NOT B | NOT C | A AND NOT B | Q
1 | 1 | 1 | 0 | 0 | 0 | 
1 | 1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 1 | 
1 | 0 | 0 | 1 | 1 | 1 | 
0 | 1 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 0 | 

## Slide 19: Worked Example 3
Now let’s add A AND NOT C.
A | B | C | NOT B | NOT C | A AND NOT B | A AND NOT C | Q
1 | 1 | 1 | 0 | 0 | 0 | 0 | 
1 | 1 | 0 | 0 | 1 | 0 | 1 | 
1 | 0 | 1 | 1 | 0 | 1 | 0 | 
1 | 0 | 0 | 1 | 1 | 1 | 1 | 
0 | 1 | 1 | 0 | 0 | 0 | 0 | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 
0 | 0 | 1 | 1 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 1 | 0 | 0 | 

## Slide 20: Worked Example 3
Now we can build up our final expression where we have a 1 in the (A AND NOT B) column, OR we have a 1 in the (A AND NOT C) column.
A | B | C | NOT B | NOT C | A AND NOT B | A AND NOT C | Q
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0

## Slide 21: Worked Example 3
Step 4: Look at the final output
So here we can see that there are only 3 possible inputs to this gate that give us an output of true:
A | B | C
1 | 1 | 0
1 | 0 | 1
1 | 0 | 0

## Slide 22: Lesson Summary
You can combine logic gates to draw Boolean expressions.
Truth tables can be used to work out the outputs of any Boolean circuit.
They can be used to work out the Boolean algebra of any circuit.
The truth tables follow four rules:
Step 1 – Build your inputs
Step 2 – Check to see if any of your inputs have been NOTed
Step 3 – Build your expressions from your initial inputs
Step 4 – Look at the final output.

## Slide 23
Copyright © 2024 KnowItAllNinja.com
This presentation and its associated worksheets are protected by copyright and are licenced for resale by KnowItAllNinja.com. No part of these publications may be reproduced, distributed, or transmitted in any form or by any means, including photocopying, recording, or other electronic or mechanical methods, without the prior written permission of KnowItAllNinja.com, except as per the terms of use.
Terms of Use
By purchasing and downloading these resources you are entering a licence agreement that allows for you to share these resources with members of a single educational institution. They must not be shared with or used by any third-party outside of the institution in any form.